## Slide 1: Group 1
Bouhadan Imad, Dellafaille Lander, Mariën Levi, Pepermans Manu, Van de Mieroop Kevin

## Slide 2: Introduction
What is ElderTrack?
What can ElderTrack do for you?
Is ElderTrack worth buying?
Eldertrack

## Slide 3: Introduction
Indoor localization (floor and room)
Outdoor localization (coördinates)
Cloud based monitoring platform
What can Eldertrack do for you?

## Slide 4: Buildup of the project
e-Compass
GPS
Indoor
Outdoor
Barometer
Temperature
Back-end
LoRaWAN
data
DASH7
RSSI + DATA
Parsing
ThingsBoard.io
Fingerprinting
Altitude

## Slide 5: Frontend
Frontend
Barometer
Temperature
Back-end
LoRaWAN (DATA)
DASH7 (Data + RSSI)
Parsing
ThingsBoard.io
Fingerprinting
GPS
e-Compass
Control
INDOOR
OUTDOOR
DASH7 (Downlink)

## Slide 6: HARDWARE

## Slide 7: DASH7

## Slide 8: Communication (INDOOR )
DASH7
Uplink: Sensordata + RSSI
  Barometer and Temperature sensor
  kNN
Downlink: Alarm when tracked person is outside
  Listen for command
ALP Command: void DASH7Message(uint8_t data[], int lengthDash7)

## Slide 9: SENSORS

## Slide 10: sensors
X-NUCLEO-IKS01A2
X-NUCLEO-IKS01A2
Barometer
Temperature sensor
Accelerometer
Magnetometer
Altitude & Temperature
Ecompass

## Slide 11: Acquiring sensor data
Barometer 11 Temperature 11 magnetometer 11 accelerometer
Read registers
Concatenate
Convert
Scale
Usable data

## Slide 12: Altitude
Indoor
Use barometer and temperature
Initial: get air pressure from weather API and use as reference
  Too many different weather models
  Not 100% accurate
  Could be used Training
Now: measure air pressure at startup and use as reference
  Calculate difference in height, taking into account temperature and change in air pressure
  Define levels

## Slide 13: SENSOR Outdoor
Ecompass
Usage of the accelerometer and magnetometer data
Algorithm based on the DT0058 Design tip by ST
Gives the direction indoor where the person is heading

## Slide 14: Implementation
Drivers for the LSM303AGR and LPS22HB
Drivers written for the LSM303AGR and the LPS22HB
Calibration (hard ironing) applied in the LSM303AGR driver
No configuration needed, sensors are init in lowest power possible
Ability to put the sensors in sleep and wake them up for a single shot measurement

## Slide 15: GPS

## Slide 16: GPS (OUTDOORS)
NMEA commands
  GPGLL : Latitude, N/S, Longtitude, E/W, Time, Data valid
  Initializing
  AT+SEND:2=“5117.1421,N,0000428.4897,E,230746.000,A,A*56”
  Optimizing: Hot start

## Slide 17: lora

## Slide 18: Communication (OUTDOORs)
LoRAWAN
B-L072Z-LRWAN1
Only activated when entering danger zone
GPS Data to gateway
AT Commands
ATZ
AT+JOIN
AT+JNS=?
AT+SEND when data comes in
Notes: Check if connection between lora-module and nucleo board
NJS = network join status, zien of lora nw joined
ATZ = microcontroller reset

## Slide 19: Control Unit
Finite State Machine (FSM)

## Slide 20: Buildup of the project
e-Compass
GPS
Indoor
Outdoor
Barometer
Temperature
Back-end
LoRaWAN
data
DASH7
RSSI + DATA
Parsing
ThingsBoard.io
Fingerprinting
Altitude

## Slide 21: Backend
Parsing
Subscribed to 3 MQTT topics:
  /tb: Dash7 data
  /loriot: LoRa data
  /localisation: RSSI values for kNN
Publishing to ThingsBoard.io with ThingsBoard API and MQTT
Remote procedure call with ThingsBoard API

## Slide 22: Backend
Parsing
Dash7 data is parsed through checking the first value:
  “M”agnetometer information:
    0-360 degrees -> changed to cardinal direction
  “B”arometer information:
    raw values from sensor -> changed to altitude
  “O”K message
    Dash7 RPC is received by node
  “E”rror message
    LoRaWAN is not joined on node
LoRa data is parsed through checking if GPS information is valid:
  “A”ctive, GPS data is valid
    change minutes to degrees and correct if GPS data is from Southern Hemisphere
kNN is calculated if RSSI values are received within one second form at least 3 gateways

## Slide 23: Backend
Thingsboard.IO

## Slide 24: Backend
Thingsboard.IO

## Slide 25: Fingerprinting
training
Define training locations 27
  26 inside + 1 outside to detect danger zone
Collect measurements 20 per location
  More measurements, higher accuracy
Set up database for comparison

## Slide 26: Fingerprinting
operational phase
2.2
2.4
3.1
3.5
2
1
1
Receive Data
Calculate Distances
Find Neighbor
Vote on labels
Natasha Latysheva (2016). Implementing Your Own kNN using Python. https://www.kdnuggets.com/2016/01/implementing-your-own-knn-using-python.html

## Slide 27: Fingerprinting
operational phase
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0
k | 10.1852 | 7.4074 | 8.3333 | 9.2593 | 9.2593 | 11.1111 | 11.1111 | 10.1852 | 9.7222

## Slide 28: Energy consumption
Low power features
Small circuits to switch the pheripherals on and off:
  GPS
  Buzzer
  Lora and Dash7
Sensors are init in sleep mode
  Only wake up on certain times, pushing data and go back to sleep

## Slide 29: Energy Consumption
Measured Energy consumption (NUCLEO + SENSORS)
Idle time
LPS22HB
LSM303AGR
Idle time
Chart: Consumption Nucleo + Sensors
| 50.0 | 50.5 | 51.0 | 51.5 | 52.0 | 52.5 | 53.0 | 53.5 | 54.0 | 54.5 | 55.0 | 55.5 | 56.0 | 56.5 | 57.0 | 57.5 | 58.0 | 58.5 | 59.0 | 59.5 | 60.0 | 60.5 | 61.0 | 61.5 | 62.0 | 62.5 | 63.0 | 63.5 | 64.0 | 64.5 | 65.0 | 65.5 | 66.0 | 66.5 | 67.0 | 67.5 | 68.0 | 68.5 | 69.0 | 69.5 | 70.0 | 70.5 | 71.0 | 71.5 | 72.0 | 72.5 | 73.0 | 73.5 | 74.0 | 74.5 | 75.0
Current (mA) (Sensors) | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 16.4 | 14 | 14 | 14 | 16.2 | 14.2 | 14 | 14 | 14 | 14.2 | 16.3 | 14 | 14 | 16.1 | 14 | 14 | 14 | 14 | 15.4 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14 | 14

## Slide 30: Energy Consumption
Measured Energy consumption (NUCLEO + SENSORS + DASH7)

## Slide 31: Extras
Watchdog timer
  Starts when main Nucleo board initializes
  If no reset within window; MCU reset
Buzzer
  Goes off when in alarm state
  While waiting for GPS coordinates

## Slide 32: Possible improvements
Only send DASH7 messages when movement is detected
Outdoor localization using height and ranging
  Calculate height with reference pressure at sea level
  Calculate distance from home using Lora (TOF, RTT)
  Height + distance Use map to determine location
Put main module in sleep mode to reduce power consumption
System working on 3.3V instead of 5V
More measurements per point for kNN improvements
GPS hot start

## Slide 33: Demonstration