## Slide 1: Group 1
Bouhadan Imad, Dellafaille Lander, Mariën Levi, Pepermans Manu, Van de Mieroop Kevin

## Slide 2: Introduction
What is ElderTrack?
What can ElderTrack do for you?
Is ElderTrack worth buying?
Eldertrack

## Slide 3: Introduction
Indoor localization (floor and room)
Outdoor localization (coördinates)
Cloud based monitoring platform
Eldertrack

## Slide 4: Buildup of the project
e-Compass
GPS
Indoor
Outdoor
Barometer
Temperatuur
Back-end
LoRaWAN
data
DASH7
RSSI + DATA
Parsing
ThingsBoard.io
Fingerprinting
Altitude

## Slide 5: Backend
Parsing
Subscribed to 3 MQTT topics:
  /tb: Dash7 data
  /loriot: LoRa data
  /localisation: RSSI values for kNN
Publishing to ThingsBoard.io with ThingsBoard API and MQTT
Remote procedure call with ThingsBoard API

## Slide 6: Backend
Parsing
Dash7 data is parsed through checking the first value:
  “M”agnetometer information:
    0-360 degrees -> changed to cardinal direction
  “B”arometer information:
    raw values from sensor -> changed to altitude
  “O”K message
    Dash7 RPC is received by node
  “E”rror message
    LoRaWAN is not joined on node
LoRa data is parsed through checking if GPS information is valid:
  “A”ctive, GPS data is valid
    change minutes to degrees and correct if GPS data is from Southern Hemisphere
kNN is calculated if RSSI values are received within one second form at least 3 gateways

## Slide 7: Backend
Thingsboard.IO

## Slide 8: Backend
Thingsboard.IO

## Slide 9: Fingerprinting
training
Define training locations 27
  26 inside + 1 outside to detect danger zone
Collect measurements 20 per location
  More measurements, higher accuracy
Set up database for comparison

## Slide 10: Fingerprinting
operational phase
2.2
2.4
3.1
3.5
2
1
1
Receive Data
Calculate Distances
Find Neighbor
Vote on labels
Natasha Latysheva (2016). Implementing Your Own kNN using Python. https://www.kdnuggets.com/2016/01/implementing-your-own-knn-using-python.html

## Slide 11: Fingerprinting
operational phase
Chart: 
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0
k | 10.1852 | 7.4074 | 8.3333 | 9.2593 | 9.2593 | 11.1111 | 11.1111 | 10.1852 | 9.7222

## Slide 12: Frontend
Frontend
Barometer
Temperature
Back-end
LoRaWAN (DATA)
DASH7 (Data + RSSI)
Parsing
ThingsBoard.io
Fingerprinting
GPS
e-Compass
Control

## Slide 13: HARDWARE

## Slide 14: Communication (OUTDOORs)
LoRAWAN
B-L072Z-LRWAN1
Only activated when entering danger zone
GPS Data to gateway
AT Commands
ATZ
AT+JOIN
AT+JNS=?
AT+SEND when data comes in

## Slide 15: GPS (OUTDOORS)
NMEA commands
  GPGLL : Latitude, N/S, Longtitude, E/W, Time, Data valid
  Initializing
  AT+SEND:2=“5117.1421,N,0000428.4897,E,230746.000,A,A*56”
  Optimizing: Hot start

## Slide 16: Communication (INDOOR )
DASH7
Uplink: Sensordata + RSSI
  Barometer and Temperature sensor
  kNN
Downlink: Alarm when tracked person is outside
  Listen for command
ALP Command

## Slide 17: sensors
X-NUCLEO-IKS01A2
X-NUCLEO-IKS01A2
Barometer
Temperature sensor
Accelerometer
Magnetometer
Altitude & Temperature
Ecompass

## Slide 18: Acquiring sensor data
Barometer 11 Temperature 11 magnetometer 11 accelerometer
Read registers
Concatenate
Convert
Scale
Usable data

## Slide 19: Altitude
Indoor
Use barometer and temperature
Initial: get air pressure from weather API and use as reference
  Too many different weather models
  Not 100% accurate
  Could be used Training
Now: measure air pressure at startup and use as reference
  Calculate difference in height, taking into account temperature and change in air pressure
  Define levels

## Slide 20: Control Unit
Finite State Machine (FSM)
DIAGRAM

## Slide 21: SENSOR Outdoor
Ecompass
Levi

## Slide 22: Implementation
Drivers
Levi

## Slide 23: Documentation
Levi

## Slide 24: Energy consumption
Low power features
Levi

## Slide 25: Energy consumption
Estimation by CubeMX
Levi

## Slide 26: Energy Consumption
Measured Energy consumption
Levi

## Slide 27: Possible improvements
Only send DASH7 messages when movement is detected
Outdoor localization using height and ranging
  Calculate height with reference pressure at sea level
  Calculate distance from home using Lora (TOF, RTT)
  Height + distance Use map to determine location
Put main module in sleep mode to reduce power consumption
More measurements per point for kNN improvements

## Slide 28: Demonstration